## Slide 1: Site-specific Wind Resource Assessment for Accurate Wind Energy Yield Calculations
Hoang Thi Giang, Vietnam Partner of Ammonit Measurement GmbH

## Slide 2: Ammonit Company Profile
German company, based in Berlin
+25 years of know-how (founded in 1989)
Projects in more than 100 countries
Measurement equipment for the following activities: Before the construction of a wind or solar power plant
- Wind Resource Assessment Measurements
- Solar Resource Assessment Measurements
- Soiling Measurement
After the construction of a power plant
- Wind Monitoring Systems (SCADA)
- Solar Monitoring Systems
- Power Curve Measurements
- Soiling Measurement
Wind Measurement
Solar Measurement
Notes: 13.05.09
2

## Slide 3: Ammonit Company Profile
Own products with own development
Data loggers  Meteo-40
Online Software for campaign monitoring  AmmonitOR
Complete first class measurement systems Wind sensors from the German company Thies
Solar sensors from the Japanese company EKO
SoDAR devices from Swedish company AQ System
LiDAR devices from UK company ZephIR Lidar
Configuration of cables, cabinets, …  designed and assembled by Ammonit
Notes: 13.05.09
3

## Slide 4: Ammonit Product Portfolio
Data Loggers |  | Anemometers |  | Wind vanes | 
Ultrasonic Anemometers |  | Barometers |  | Temperature & Humidity Sensors | 
Pyranometers Pyrheliometers Sun Trackers / RSI |  | Precipitation |  | Remote Sensing Systems | 
Steel Cabinets |  | Communication & Power Supply Systems |  | Obstacle Lights | 

## Slide 5: Ammonit Global Partner Network
Ammonit cooperates with local partners for:
Assembly of systems (cables, solar supply, ...)
Mast and system installation
Maintenance of the system
Ammonit Partner in Vietnam
Thinh Phong Ltd. E-mail: thinhphongndv@gmail.com

## Slide 6: Ammonit References for Wind Resource Assessment (I)
Egypt
Bulgaria
USA
Iran
Pakistan
Turkey
Uruguay
Finland

## Slide 7: Ammonit References for Wind Resource Assessment (II)
SoDAR in Chile
LiDAR in Switzerland
SoDAR in Germany
LiDAR in Germany
LiDAR in Germany
SoDAR in Sweden

## Slide 8: Ammonit References for Solar Resource Assessment
Egypt
Egypt
Brazil
Chile
Mexico
Egypt

## Slide 9: Wind Power Potential in Vietnam
Good and great potential for wind energy generation with approx. 3,000 km coastal line
Existing wind atlas whereas the data quality is insufficient for energy yield calculations  Site-specific measurements for accurate bankable energy yield calculations necessary

## Slide 10
Wind measurement – Why?
Wind Resource Assessment Wind Farm Monitoring
Climate Research
Photo by GIZ: Wind site assessment in Northern Chile

## Slide 11: Why Wind Measurement is important?
Commercial view
Wind resource assessment to design profitable wind farms
Wind farm monitoring to ensure high productivity
Site monitoring to organize efficient maintenance schedules
Meteorological and governmental view
Wind maps
Climate research

## Slide 12: International Standard for Wind Power Performance Measurement
Standards + Guidelines
IEC 61400-12-1 (2017) „Power Performance Testing”
Set-up of a met mast including installation of sensors, sensor quality regarding accuracy and reliability
MEASNET (2016) „Evaluation of site specific winds”
Process of site assessment incl. data collection, evaluation and interpretation
Criteria for data quantity and quality, as well as reporting
Focus on data quality, plausibility and integrity incl. data filtering and reporting
 Fulfilled with Ammonit Measurement Systems
Quality criteria for SoDAR / LiDAR devices and ultrasonic anemometer for wind assessment / traceability of measurement data
 Fulfilled with Ammonit Measurement Systems
Notes: 18.09.09
12

## Slide 13: Betz Law
Wind speed
Wind energy is proportional to the cube of the wind speed according to Betz’ law: Wind power is P = 1/2 • ρ • A • v³ Δ1% wind speed ≈ Δ 3% wind energy
Measure the wind conditions to calculate the wind energy
A is the area;
ρ is the air density, ρ = p / (R • T), being p the air pressure, T the air temperature and R the gas constant;
v is the wind speed
Notes: 18.09.09
13

## Slide 14: Why high quality measurement equipment?
Leverage Effect: Impact of measurement error on profitability
A small error in the energy assessment has a huge impact in the profitability of a project.
wind
measurement
(error)
energy
assessment
(error)
profitability
calculation
(error)
1st leverage effect
2nd leverage effect
v
P
P
$$$$$
P = 1/2 • ρ • A • v³
1% wind speed error => 3% wind energy error

## Slide 15: Impact of Measurement Errors on Estimated Annual Energy Production (AEP)
Comparison of the Impact of Different Wind Sensors on the Assessment
Reduce measurement errors by installing high quality sensors
Even small discrepancies in the evaluation of wind speed data lead to significant deviations in the assessment calculations
 | Generated Energy Error by 1% Measurement Error | Notes
Anemometer | Δ1% wind speed  Δ3% energy | Most important measurement
Wind vane | No direct relation, but eventually wrong wind farm design | Important measurement for wake effect
Barometric pressure sensor | Δ1% pressure  Δ1% energy | Extrapolation of pressure possible once site is known
Temperature sensor | 1°C  0.35% | 
Humidity sensor | with 40°C; 1%  0.05% | 
Notes: 18.09.09
15

## Slide 16: Calibration Service via Ammonit Wind Tunnel GmbH
New company founded by Ammonit Measurement GmbH and Wind-consult GmbH
Independent test laboratory according to DIN EN ISO / IEC 17025
Accredited by DAkkS and certified by MEASNET
Became a member of MEASNET Group in April 2017
Benefit from sensor calibration at Ammonit Windtunnel
  Faster service
  Better prices than other Germany calibration institutes
  Calibration of cup anemometers, wind vanes and ultrasonic anemometers
  Download of calibration certificates via website of Ammonit Windtunnel
  Calibrated sensors available on stock

## Slide 17: Remote Sensing Devices for Wind Resource Assessment and Monitoring
SoDAR AQ 510 Windfinder
SoDAR = Sound Detection And Ranging
Doppler effect  outgoing sound beams reflected by the aerosols in the wind flow
Fully classified acc. to IEC 61400-12-1:2017
Wind speed and direction measurement between 40 … 200 m
LiDAR ZephIR 300
LiDAR = Light Detection And Ranging
Doppler effect  outgoing laser beam reflected by the aerosols in the wind flow
Fully classified acc. to IEC 61400-12-1:2017 with finance-grade data accepted by DNV GL
Wind speed and direction measurement between 10 … 200 m
Notes: 18.09.09
17

## Slide 18
Solar measurement Why and how?
Notes: 18.09.09
18

## Slide 19: Solar Measurement
Commercial view
Solar resource / site assessment to design profitable PV / CPV / CSP power plants
Site monitoring to organize efficient maintenance schedules and to ensure high productivity
Meteorological and governmental view
Solar maps
Climate research
Solar power plants
PV = Photovoltaic
CPV = Concentrated Photovoltaic
CSP = Concentrated Solar Power

## Slide 20: Solar Irradiation
Global Irradiation = Diffuse + Direct
GHI = DHI + DNI • cos(θ)
Where θ is the zenith angle (at vertical over the site 0˚, at horizon 90˚).
GHI = Global Horizontal Irradiation
DHI = Diffuse Horizontal Irradiation
DNI = Direct Normal Irradiation
GTI = Global Tilted Irradiation
Diffuse (20%)
Direct (80%)
Global (100%)
+
=
W/m²
DIRECT
(DNI)
DHI
DIFFUSE
DNI * COS (Ө)
Ө
Notes: 18.09.09
20

## Slide 21: Ammonit Meteo-40 Data Logger – Different Applications
Wind and Solar Maps
Wind Resource Assessment
Solar Resource Assessment
Climate Research
Wind Farm Monitoring (SCADA)
Solar Power Plant Monitoring
Site Assessment in Cold Climate
Soiling Measurement

## Slide 22: Ammonit Meteo-40 Data Logger
Storage of 1 sec. original measurement data (up to 2 GB)*
   Turbulence analysis, wind gust and mechanical load calculations
Recording of electrical and physical data
   Retrospectively correction of possible mistakes by applying slope and offset
Digitally signed and encrypted measurement data*
   Prevent data manipulation and unauthorized data access
Flexible Communication: UMTS/GSM/CDMA/GPRS, RS485, WiFi, Ethernet, USB
   Laboratory and on-site communication
Configurable data transfer via HTTPS, FTP/SCP, email to AmmonitOR or client server*
   Security purposes
* according to MEASNET Site Assessment Norm

## Slide 23: Meteo-40 Web Interface: Sensor Configuration
User-friendly web interface for sensor configuration
  Detailed sensor library
  Sensor helper (wizard) for convenient configuration

## Slide 24: Meteo-40 Web Interface: Communication Configuration
Various methods to transfer and download measurement data:
  File upload via FTP or SCP  upload to AmmonitOR for campaign monitoring
  Send CSV files as email attachment
  Download CSV files via web interface
  Download CSV files on USB memory drive on-site
Schedule to configure file uploads and online periods
Convenient modem configuration via provider helper (wizard)

## Slide 25: Ammonit Meteo-40 Data Loggers: Remote Access
Internet
Ammonit Tunnel Server
Ammonit
Tunnel Server
Ammonit Tunnel Server provides IP address, at which Meteo-40 can be reached on the Internet (e.g., https://subdomain.tunnel.ammonit.com)
Communication via Ammonit Tunnel
Data transfer via HTTPS connection

## Slide 26: Ammonit Meteo-40 Data Logger for SCADA Operation
SCADA = Supervisory Control and Data Acquisition
Monitoring the performance of a wind and solar farms
Verification of the predicted annual energy production
Communication via Ethernet (TCP/IP) or RS485
Data transmission via standard protocols Modbus TCP/IP and Modbus RTU
Comparison of meteorological data gathered by wind measurement systems and data from the wind turbine
Notes: 13.05.09
26

## Slide 27: AmmonitOR: Managing & Monitoring Measurement Campaigns
Notes: 18.09.09
27

## Slide 28: AmmonitOR: Managing & Monitoring Measurement Campaigns
Management and monitoring of measurement campaigns (solar, wind, power curve)
Data quality check according to MEASNET site assessment guideline
    Filters to detect measurement errors or sensor defects
    Calendar to monitor data integrity
Evaluation and reporting
    Display data in customizable plots over certain periods
    PDF reports on sensors and statistics
Data archiving
Notes: 18.09.09
28

## Slide 29: Ammonit solutions for data security
E-mail
Server
Download
OR
Current research project

## Slide 30: Contact
Thank you!
Ammonit Measurement GmbH
Wrangelstrasse 100 • D-10997 Berlin (Germany)
T: +49 30 6003188-0
F: +49 30 6003188-10
info@ammonit.com
www.ammonit.com
Please contact us for further information